REZ.COM Quick Reference

R	Read file. Entered as Rxxx.COM, Rxxx.SYM or Rxxx.CTL. This must be done after starting REZ.com itself. Don’t make command-line specifications. Start up REZ First and then tailor your session.

S	Save file. Entered as Sxxx.ASM, Rxxx.SYM or Rxxx.CTL. The response to entering the Save command for the CTL or SYM file will occur immediately, but the “saving” of the ASM file is actually a generating process.

When you enter “Sxxx.ASM”, you will open up the ASM file, but you must then execute the List command, in the form of Ls,e to actually put the generated assembler code to the file. When the List command completes, enter “Z” at the command prompt to close the ASM file.

X	(Y/N)Purge SYM & CTL tables ?

This command is useful in CTL data building sessions where it’s important to get rid of  bunch of symbols, but you want to keep the Ctl formatting. Save CTL, Purge all, Read CTL and then re-Build SYM

T	Toggle TRIM On/Off (On = Labels appear on instruction, as opposed to being on their own line.

O	Set Offset to where code will actually be loaded, and subsequently how much space you’ve allocated to the CTL table. Better a bit too much offset than to overwrite the front end of your code. The default offset is 4000H, which is good, but for most code disassemblies, I find o6000h to be a better bet.

?	Dump stats

B	Build code (Also entered as Bs,e where s = starting addr and e = End addr, in hex digit (0,1,2,3…,A,B,C,D,E,F).

L	List code (Also entered as Ls,e where s = starting addr and e = end addr, in hex digit (0,1,2,3…,A,B,C,D,E,F).

Also used after entering the Save command for the .ASM file to cause rez to build data to the file.

A	Assemble code. Similar to the List command. (Also entered as As,e where s = starting addr and e = end addr, in hex digit (0,1,2,3…,A,B,C,D,E,F).

D	Dump storage to console (Also entered as ds,e where s = starting addr and e = end addr, in hex digit (0,1,2,3…,A,B,C,D,E,F).

C	CTL table list or entry. Using just the C char on the command line will cause the CTL table stats to be displayed.

You can toggle the definition of an area my entering your own CTL entry by entering Ca,f where a=addr in code and

f=function. Functions supported are…

I – Start instruction string

B – start of DB, single byte format

W – start of word format data.

S – Begining at addr, make data DS (existing data ignored)

E – make end at addr

K – kill CTL entry for addr

SAMPLE SESSION

A0>rez      (========================Use this to start REZ

RESOURCE by Ward Christensen

Z-80 – Zilog Version 4.1

Restart 103h!!

19.03.85

Memory open to ECFF

<*>o6000   (======================== don’t use default of 4000, set to 6000

<*>?     (========================== ask for status display

SYMTBL=2800 2800

PC    =0100

OFFSET=6000

MEMTOP=ECFF

CTLTBL=2100 2100

<*>rrez.com  (====================== now load code,

7F80 1F80   (======================= code actually at 6000-7F80,

<*>D0100    (======================= show me dump, start at 0100H

0100: C3 06 01 C3 B6 01 AF 32 FB 1F 32 FD 1F CD 6F 01 .......2..2...o.

0110: 52 45 53 4F 55 52 43 45 20 62 79 20 57 61 72 64 RESOURCE by Ward

0120: 20 43 68 72 69 73 74 65 6E 73 65 6E 0D 0A 5A 2D  Christensen..Z-

0130: 38 30 20 2D 20 5A 69 6C 6F 67 20 56 65 72 73 69 80 - Zilog Versi

0140: 6F 6E 20 34 2E 31 20 0D 0A 52 65 73 74 61 72 74 on 4.1 ..Restart

0150: 20 31 30 33 68 21 21 20 0D 0A 31 39 2E 30 33 2E  103h!! ..19.03.

0160: 38 35 24 FD E5 DD E5 CD 05 00 DD E1 FD E1 C9 D1 85$.............

0170: 0E 09 CD 63 01 21 00 00 39 22 FE 20 31 FE 20 CD ...c.!..9". 1. .

0180: A3 1E 0D 0A 4D 65 6D 6F 72 79 20 6F 70 65 6E 20 ....Memory open

0190: 74 6F 20 00 2A 06 00 2E 00 2B 22 75 1F CD C4 1C to .*....+"u....

01A0: CD 04 1E CD 04 1E 21 00 00 22 79 1F CD B7 1E AF ......!.."y.....

01B0: 32 66 1F 32 68 1F 31 FE 20 CD 5F 1E 11 7D 1F 1A 2f.2h.1. ._..}..

01C0: FE 0D 20 0F 3A 38 1F CD F2 01 20 E3 F5 3E 0D 32 .. .:8.... ..>.2

01D0: 7E 1F F1 21 FE 01 01 13 00 ED B1 20 5A F5 CD F2 ~..!....... Z...

01E0: 01 28 02 3E 2A 32 38 1F F1 09 09 09 4E 23 46 EB .(.>*28.....N#F.

01F0: C5 C9 FE 4C C8 FE 44 C8 FE 42 C8 FE 41 C9 3B 41 ...L..D..B..A.;A

<D>L100,112  (==========list code, instr format starting at 0100h

0100		JP	0106H

0103		JP	01B6H

0106		XOR	A

0107		LD	(1FFBH),A

010A		LD	(1FFDH),A

010D		CALL	016FH

0110		LD	D,D  (====from dump, start of constant-in-storage

0111		LD	B,L

<L>C100,I  (=============== we do this to be unambiguous

<*>c110,b  (=============== flip over to DB generation

<*>L100    (=============== now let’s see what we got

0100		JP	0106H

0103		JP	01B6H

0106		XOR	A

0107		LD	(1FFBH),A

010A		LD	(1FFDH),A

010D		CALL	016FH      (===== looks like addr where code resumes

0110		DB	‘RESOURCE by Ward Christensen’

012C		db	0DH,0DH

012E		DB	‘Z-80 – Zilog Version 4.1 ‘

0147		db	ODH,OAH

0149		DB	‘Restart 103h!!’

0158		db	ODH,OAH

015A		DB	‘19.03.85$’

0163		db	0FDH,0E5H,0DDH,0E5H,0CDH,0DDH

016B		db	0E1H,0FDH,0E1H,0C9H

016F		db	0D1H,0EH,9,0CDH

<*>C016F,I  (=====set a flip back to instruction-stream mode

<*>L100  (=======let’s look again and see what we got

0100		JP	0106H

0103		JP	01B6H

0106		XOR	A

0107		LD	(1FFBH),A

010A		LD	(1FFDH),A

010D		CALL	016FH

0110		DB	‘RESOURCE by Ward Christensen’

012C		db	0DH,0DH

012E		DB	‘Z-80 – Zilog Version 4.1 ‘

0147		db	ODH,OAH

0149		DB	‘Restart 103h!!’

0158		db	ODH,OAH

015A		DB	‘19.03.85$’

0163		db	0FDH,0E5H,0DDH,0E5H,0CDH,0DDH

016B		db	0E1H,0FDH,0E1H,0C9H

016F		POP	DE  (========this looks good, but…

0170		LD	C,9

0172		CALL	0163H   (=====looks like code starts at 0163H

0175		LD	HL,0

0178		ADD	HL,SP

<L>c163,I (===================Say that the code starts earlier than 016F

<*>L100  (=======show product

0100		JP	0106H

0103		JP	01B6H

0106		XOR	A

0107		LD	(1FFBH),A

010A		LD	(1FFDH),A

010D		CALL	016FH

0110		DB	‘RESOURCE by Ward Christensen’

012C		db	0DH,0DH

012E		DB	‘Z-80 – Zilog Version 4.1 ‘

0147		db	ODH,OAH

0149		DB	‘Restart 103h!!’

0158		db	ODH,OAH

015A		DB	‘19.03.85$’

0163		PUSH	IY

0165		PUSH	IX

0167		CALL	5

016A		POP	IX

016C		POP	IY

016E		RET

016F		POP	DE

<L>

:

:

<*>B100,2100  (= code and constants mapped, now B to “build” symbols table

but extend upper address, here beyond where the program

code ended at 1F80H. This allows REZ to account for

areas beyond the actual end of the code where lousy

programming practices allow for this type of mischief.

:

a flurry of screen activity ensues…

:

<*>L100  (=======let’s look again and see what we got

0100  t0100:	;0100  (== this and many other symbolics gen’d…

JP	0106H

0103		JP	01B6H

0106  j0106:	;0106

XOR	A

0107		LD	(1FFBH),A

010A		LD	(1FFDH),A

010D		CALL	016FH

0110		DB	‘RESOURCE by Ward Christensen’

012C		db	0DH,0DH

012E		DB	‘Z-80 – Zilog Version 4.1 ‘

0147		db	ODH,OAH

0149		DB	‘Restart 103h!!’

0158		db	ODH,OAH

015A		DB	‘19.03.85$’

0163  c0163:		;0163

PUSH	IY

0165		PUSH	IX

0167		CALL	c0005	;5

016A		POP	IX

016C		POP	IY

<*>T  (===================toggle trim ON

Trim On (===this means put symbolics in same line as assembly code

<*>L100

0100  t0100:	JP	0106H   (===== Name-on-instr-line, from TRIM

0103		JP	01B6H

0106  j0106:	XOR	A  (==== same here

0107		LD	(1FFBH),A

010A		LD	(1FFDH),A

010D		CALL	016FH

0110		DB	‘RESOURCE by Ward Christensen’

012C		db	0DH,0DH

012E		DB	‘Z-80 – Zilog Version 4.1 ‘

0147		db	ODH,OAH

0149		DB	‘Restart 103h!!’

0158		db	ODH,OAH

015A		DB	‘19.03.85$’

0163  c0163:	PUSH	IY

0165		PUSH	IX

0167		CALL	c0005	;5

016A		POP	IX

016C		POP	IY

016F  c016F:	POP	DE

<L>?  (==================just to see how the stats changed

SYMTBL=2800 3428

PC    =0170

OFFSET=6000

MEMTOP=ECFF

CTLTBL=2100 2220

<*>srez.ctl (===== save our CTL table. It’s worth the effort.

<*>srez.asm (===== we sure want to do this !

++WRITING .ASM ENABLED

USE Z COMMAND OR E CONTROL TO CLOSE FILE++

<*>L100,2100

:
another flurry of screen activity as the code is “listed” to the .ASM file.

:

<*>Z

- END

++ ASM FILE CLOSED++

<*>^C  (==========bail out here

A0>REN REZ.MAC=REZ.ASM  (====rename output so Macro-80 can digest

:

:

; modify code to add “.z80” header to enable z80 compiles

; and an org statement, starting at 0100h to make the comp[iled

; output match up in comparison to the symbolic names

;

A0>M80  (===start up m80 first, otherwise we might see “invalid machine

opcode” abend under MyZ80. I suspect it’s a parity setting

discrepancy between the 8080 code and the z80 engine. This

seems to bypass the issue.

*=REZ/M/L  (====this will generate listing to .PRN file

*^C  (=== bail out of Macro-80

A0>

Enjoy !

Mark E Sharafinski

MarkSrph@aol.com